## Slide 1: Experiment “Prep Talk”
Silas Oettinghaus
CAU - Polariton

## Slide 2
Modulator Characterization
Bias optimization
  Stability of bias (Temp., Pol., Drift, …)
  Influcence of bias on BER
Transmission Experiment

## Slide 3: Modulator Characterization
Transfer characteristics dependent on optical wavelength of input ()
Optimal operating wavelength has to be found before use:
  Find input polarization state such that the output power is maximum for this
  Tune in a wide range (here:1300nm  0.05nm  1320nm)
  Record output power
  Locate maximum in wavelength area of interest
  Choose operating point at -3 dB from maximum (= quadrature point)

## Slide 4: Setup for Modulator Characteristics Measurement
Tunable Laser
(ECL, Tunics T100)
Up to 10 dBm
Tunable in 0.01 nm steps
Keysight
Attenuator/PM
N7764A
Pol.
Control
Modulator

## Slide 5: Transfer Characteristics 3 / 3

## Slide 6: Bias Optimization (Example)
PAM 4
PAM 6
PAM 8
Wants extinction
Wants linearity

## Slide 7: Kiel University Equipment
110 GHz
-10 dB IL
3.2 V Vpi
256 Gsa/s
256 Gsa/s
70 GHz
10 dBm
O-band tunable
Laser | Modulator | AWG | Fiber | PDFA | PD | Scope
EXFO OSICS T100 External Cavity Laser | Hyperlight O-Band TFLN | Keysight M8199B | SSMF 1-10 km | Thorlabs PDFA100 | Fraunhofer PIN Single Ended | Keysight UXR1104B
1292nm,…,1327nm 10 dBm | 110 GHz 3.2 V Vpi 10 dB IL | 256 Gsa/s | ZDW ~1310 nm |  | 70 GHz | 110 GHz
PDFA

## Slide 8: Setup for High-Speed Transmission
AWG Keysight M8199B
256 GS/s
80 GHz bandwidth
Tunable Laser
(ECL, Tunics T100)
Up to 10 dBm
Tunable in 0.01 nm steps
PM
SOA
PDFA
Tunable Optical
Bandpass Filter
PIN
Photo Diode
70 GHz
bandwidth
Pol.
Control
Modulator
Probe
PM
Scope
Keysight
UXR 1102A
OSA
256 GS/s
110 GHz bandwidth
10%
PM: Eigenlight power meter + tunable attenuator
Mainly used to adjust center frequency of OBF

## Slide 9
-10 dB @ 75 GHz
-20 dB @ 92 GHz
-30 dB @ 101 GHz
448 Gbps
224 GBd PAM 4 = 112 GHz
180 GBd PAM 6 = 90 GHz
150 GBd PAM 8 = 75 GHz
75
90
112

## Slide 10: DSP Structure (during experiment)
VNLE + PF + MLSE
DB precoded
DB encoded
Low or no precompensation
„Full“ pre compensation
Maintains high Vpp
wants linear bias in quadr. point
„Full“ pre compensation